## Slide 1: To Design an Efficient MAC Protocol for Underwater Acoustic Sensor Network under Multi-hop Environment

## Slide 2: introduction
My Goal: To design a efficient MAC protocol for underwater acoustic sensor network suitable for multi-hop network
Different emphasis from mid-semester surveys:
Challenges and opportunities of Physical channel of underwater communication(already discussed)
Studied different MAC protocol as introduced by different authors→ (already discussed)
Comparison between MAC’s and their challenges (already discussed)

## Slide 3: Agenda of Present work
  Introduction to T-Lohi ( A new mac protocol for underwater communication)
  Flavours of T-Lohi
  State transition diagram of T-Lohi
  Pseudo code of T-Lohi
  Performance evaluation
  Drawback and modification
  Proposed MAC protocol

## Slide 4: Tone-Lohi (T-Lohi) Protocol
Alternating reservation and data periods
Data period reserve by :
  Transmitting short tones and……
  Listening for maximum propagation time (330ms) i.e. contention period (CP)
  Successful reservation if a single tone is sent in a CP
  Back-off when other tones detected

## Slide 5: Novel Ideas
Exploit hardware wake up using short (<5ms) tones:
  Little energy cost of listening over long periods
  Short duration; thus low collision probability
Detect and count other contenders (if they exist )
  Collision detection (CD,like Ethernet) leads to good utilization, independent of load
  Use contender count to adopt back-off to traffic, improving fairness

## Slide 6: Synchronized T-Lohi (ST-Lohi)
Synchronized CPs, and tone sent only at the beginning
  Synchronization removes uncertainty in time
  Waiting the entire CP removes uncertainty in space
If contention detected in a CP, nodes back off:
  Nodes that loose will have higher priority to transmit in the next reservation period
After data period ends, nodes attempt reservation based on traffic estimates from previous reservation period

## Slide 7: aUT and cUT-Lohi
cUT-Lohi allows transmission at any time
  Long contention round duration
  Worst case: CRcUT = 2 Гmax + 2Ttone
  Worst case contender A transmit at: tc +Ttone+ Гmax –Є, just before it hears C’s transmission
aUT-Lohi reduces CRsUT to just maximum propagation delay
  Shorter contention duration
  Does not guarantee detection!
  CRaUT = Гmax + Ttone

## Slide 8: State transition diagram of T-Lohi

## Slide 9: Pseudo code of T-LOhi

## Slide 10: Performance Evaluation
Channel Utilization = Ptx\ (Ptx + CR)
  (i.e. ratio of data to frame length)
µ = Ptx\ CR
  (i.e. the packet duration time in multiples of contention rounds)
THmax = µ\ (µ+1)
(i.e. maximum throughput)
Let packet transmission duration, Ptx = 650ms
Result: the maximum utilization of T-Lohi increases with shorter CR caused by shorter communication range, lower bandwidth, or longer packet size
r

## Slide 11: Throughput as Load varies
Simulation parameter: 300*400m area for a fully connected network, acoustic modem with 500m range. Data rate 8kb\s and packet length 650bytes
Packet transmission duration Ptx = 650ms
Tone detection = 5ms
CRst = Гmax + Ttone
CRcUT = 2 Гmax + 2Ttone
CRaUT = Гmax + Ttone

## Slide 12: Observation
T-lohi is very efficient at low offered load where contention rate are low. When the load is less than 0.5packets\s, T-lohi is very close to maximum theoretical utilization
As offered load approaches the practical capacity (0.5-1packet\s), calculation shows that T-Lohi reaches about 50% of maximum utilization
Throughput increases monotonically with packet length or µ

## Slide 13: Modification of T-Lohi
Our study shows that T-Lohi MAC protocol is suitable for single hop network
For multihop network certain modification has to be required since in present T-Lohi as the load increases throughput remains stable
In our work, we propose a new MAC protocol which work efficiently in multi hop environment

## Slide 14: State transition Rules of proposed MAC protocol
state | Receive RTS | Receive CTS | Overhears xRTS | Overhears xCTS | Timer Expired
IDLE | Transmit: CTS WFDATA | Disregard packet | QUITE_RTS QUITE | QUITE_CTS QUITE | 
CONTEND | Transmit: CTS WFDATA | Disregard packet | QUITE_RTS QUITE | QUITE_CTS QUITE | Transmit: RTS WFCTS
WFCTS | Disregard packet | Transmit: DATA Sent data-> IDLE | Disregard packet | QUITE_CTS QUITE | Backoff for retransmit IDLE
WFDATA | Disregard packet | Disregard packet | Disregard packet | Disregard packet | …………….. IDLE
QUITE | Disregard packet | Disregard packet | QUITE | QUITE | …………… IDLE

## Slide 15: Backoff Algorithms
<number>
When collision occurs, node A pick up a random number T from [1,Bo], then retransmits RTS after Tbk time unit
  Tbk = uniform {0,Bcnt}*{Trts +Гmax }
How to determine Bo
  After each collision Bo_new = Fun_inc(Bo_old)
  After each successful transmission Bo_new = Fun_dec(Bo_old)
Binary exponential backoff (BEB) algorithm
  Fun_inc(Bo_old)=min{2*Bo_old, Bo_max}
  Fun_dec(B_old)=Bo_min

## Slide 16: More Details for Proposed MAC
<number>
from IDLE state, A goes to CONTEND state when it has packet to send
A sends out RTS and set a timer to 2Гmax+Tcts and transit to WFCTS state
  If A receives CTS before timer go to zero, reset its Bcnt  Bmin and sends data packet .After that A goes to WFDATA state and set timer to 2Гmax+Tdata
  Otherwise, A assumes there is a collision at B
    Increase the backoff counter interval, Bcnt, acc to BEB scheme
        Bcnt  min { 2* Bcnt, Bmax }, upon collision
        Otherwise Bcnt  Bmin, upon successful transmission
    Send next RTS after the backoff counter value
  To avoid packet collision, every neighboring node stay in QUITE state upon overhearing any xRTS or xCTS packet
  Depending upon the overheard control packet , a neighboring node set its silent duration to either QUITE_RTS or QUITE_CTS
B sends out CTS, then set a timer to 2Гmax+Tcts and transit to WFDATA state
  If data packet arrives before timer go to zero, reset its Bcnt  Bmin
  Otherwise, B disregard any control packet received while it is in WFDATA state
C overhears A’s RTS, set a timer which is long enough to allow A to receive CTS. After the timer goes to zero, C will be backoff based on BEB scheme
D overhears B’s CTS, set a timer which is long enough to allow B to receive data packet.

## Slide 17: Simulation Method
I have planned to do simulation with a multi hop network grid comprising of 16, 25 or 32 nodes
  calculate the effect of different data packet size
  Calculate the effect of different grid size
Then only I can observe the efficiency, throughput and channel utilization of the proposed protocol

## Slide 18: Conclusion
Studied different MAC protocol for underwater acoustic sensor network and go through with advantages and disadvantages. MAC design for UW-ASNs faces significant challenges. Then studied T-Lohi a new reservation based MAC protocol which is energy efficient, flexible and stable medium access for acoustic network. But it is not suitable for multi hop network , so I have proposed and study a new MAC protocol which is an adaptation of terrestrial MACA for multi hop network.
Our future work for proposed MAC protocol will include simulation result of its throughput, investigation of unfairness in the back off algorithm as well as theoretical analysis of the throughput and delay characteristics

## Slide 19: References
[1]Affan A. Syed, Wei Ye, and John Heidemann, “T-Lohi: A new class of MAC protocols for underwater acoustic sensor networks”. In Proceedings of the IEEE Infocom, pages 231–235, Pheonix, AZ, April 2008.
[2]Affan A. Syed , Wei Ye, Member, John Heidemann, “Comparison and Evaluation of the T-Lohi MAC for Underwater Acoustic Sensor Networks”
[3]M. Molins and M. Stojanovic, “Slotted FAMA: A MAC protocol for underwater acoustic networks,” in Proceedings of the IEEE OCEANS’06 Asia Conference, Singapore, May 2006.
[4]K. Sanzgiri, I. D. Chakeres, and E. M. Belding-Royer, “Determining intra-flow contention along multihop paths in wireless networks,” in Proceedings of BROADNETS’04. IEEE Computer Society, 2004
[5] Hai-Heng Ng, Wee-Seng Soh, Mehul Motani.” A Media Access Protocol for Underwater Acoustic Networks” supported by the Ministry of Education of Singapore, AcRF Tier 1 funding, under Grant No. R-263-000-370-112.

## Slide 20: THANK YOU