## Slide 1
Notes: <number>

## Slide 2: Contents
Introduction.
Introduction to 2-D Fourier transform.
Types of Frequency -Domain filters.
Basic steps in Frequency-Domain filtering.
Frequency-Domain filters for smoothing of images.
Frequency-Domain filters for sharpening of images.
Spatial -Domain filtering through High Boost filter.
Applications.
Advantages & Disadvantages.
Conclusion.

## Slide 3: Introduction
Image Enhancement?
It is the process of making an image more pleasable than the original image.
Why needed?
Noise introduced in to the image, out-of focus , atmospheric conditions, latency of imaging hardware.

## Slide 4: Introduction to 2-D Fourier transform
The 2-D DFT of input image f(x, y) is given by
where, u=0,1,2……..M-1 ; v=0,1,2……..N-1
The inverse 2-D DFT of output image F(u , v) is given by
where, x=0,1,2…….M-1; y=0,1,2……..N-1

## Slide 5: Basic steps in Frequency-Domain Filtering
Includes multiplication of input/output images by (-1)x + y

## Slide 6: Pre and Post processing steps
In this the spectrum origin is shifted to center by multiplying input and output image with (-1)x + y

## Slide 7: Types of Frequency-Domain Filters

## Slide 8: Frequency-Domain Filters for Smoothing of images
Ideal Low pass filter
Butterworth Low pass filter
Gaussian Low pass filter

## Slide 9: Example of Gaussian Low pass filtering
Character recognition in machine perception join the broken character segments with a Gaussian low pass filter with D0=80.

## Slide 10: Frequency-Domain Filters for sharpening of images
Ideal high pass filter
Butterworth high pass filter
Gaussian high pass filter

## Slide 11: Example of Gaussian High pass filtering
The edge detection is performed here. The cells shape is visible clearly after Gaussian high pass filtering.
original image high pass filtered image (Do=30)
Notes: <number>

## Slide 12: Implementation Spatial domain filtering
When operation is performed directly on the pixels of an image, then is called Spatial Domain Filtering.
When operation is performed on
the input image by a suitable transfer
function we get the required output
Image.

## Slide 13: Spatial domain filtering through High Boost filter
High boost filtering is a generalization of Unsharp Masking.
Unsharp Masking is simply a sharp image generated from blurred image of itself.
High Boost filtering generalizes this by multiplying f(x, y) by
a constant A , amplification factor.
A≥1

## Slide 14: Spatial (TIME) domain filtering through High Boost filter
Thus, High-boost filtering gives us the flexibility to increase the contribution made by image to the enhanced image.
original image high pass image(Do=30) high-boost image(A=2.5)

## Slide 15: Applications
Medical imaging.
Satellite imaging.
Material testing in industries.
Fingerprint identification.
Printing and publishing industry.

## Slide 16: Advantages & Disadvantages
Advantages:
It is simple and easy to implement.
It provides flexibility in the design of filtering solutions.
Disadvantages:
A person needs knowledge in many fields to develop an application using image processing.
Noise cannot be eliminated completely.

## Slide 17: Conclusion
Thus, image enhancement techniques in frequency domain improves the desired features of an image based on the requirements of the applications.
Notes: <number>

## Slide 18: References
Gonzalez and Woods, Digital Image Processing.
Rudra Pratap, Getting Started With Matlab 7.
P.Ramesh Babu, Digital Image Processing.
www.wikipedia.com
www.mathwork.com