## Slide 1: NANOTECHNOLOGY FOR WATER TREATMENT

## Slide 2
Contents:
Nanotechnology.
Nanomaterials in water treatment system.
Products in market.
Risks, challenges and opportunities.
Conclusion.
References.

## Slide 3: > Deals with manufacturing or manipulation of materials at nanoscale(10-9m). > Has applications in many different fields, like electronics, medical, energy sector, environmental remediation. > Being evaluated in water treatment processes in recent years > Materials having nanoscale dimensions referred to as Nanomaterials.
>
NANOTECHNLOGY

## Slide 4
FULLERENES
Composed entirely of Carbon.
Spherical, Ellipsoid or Tube shaped
Spherical fullerenes – Bucky balls.
Tubular fullerenes – Nanotubes.
Carbon nanotubes.
Buckyball

## Slide 5
NANOPARTICLES
Metallic, ceramic or inorganic.
Dimensions 1-100nm.
Large surface area, very reactive.
Exhibit interesting mechanical, magnetic, optical, chemical properties.
Borosilicate glass nanoparticles.
Borosilicate glass nanoparticles.
ecole Polytechnique Fédérale de Lausanne

## Slide 6: NANOMATERIALS IN WATER TREATMENT SYSTEMS
Nanofilters:
Made of carbon nanotubes.
Pore size: 0.0001-0.001μm.
Can remove virus, bacteria, suspended solids, large multivalent ions, dissolved organics, herbiscides, pesticides etc.
Greater efficiency compared to microfilters and ultrafilters.
Energy usage – Low.
Operating cost – Rs. 10-20 per 1000 liters.[2]
Useful in desalination operations. Being used for desalination in Israel & certain U.S. Municipalities notably Long Beach, California Municipal Water District.[1]
Nanofilter.
Developed by Argonne National Laboratory [3]

## Slide 7
Seawater Desalination – The Long Beach Method[4]
Seawater filtered to remove suspended solids.
Stage 1: Filtered seawater pumped under high pressure through nanofiltration membrane.
Only smallest 12% of salt molecules pass through
Stage 2: Water from Stage 1 is pumped under lower pressure through second nanofiltration
Membrane.
Blocks passage of almost all remaining salts.
High quality potable water produced.
Energy savings:
Traditional desalination method pressure required for pumping: 1000pounds per square inch(psi).
Long Beach Method:
525psi first stage, 250psi second stage.
Energy savings: 20-30%
Pilot plant running from 2001.

## Slide 8
2.Nanosorbents:
Used majorly in water remediation. For removing inorganic and organic pollutants, from contaminated water.
Nanoparticles used as sorbents.
Nanoparticles can be functionalized with various chemical groups to increase their affinity towards target compounds.
Nanocrystalline zeolites can remediate water containing cationic species such as ammonium and heavy metals. As well chemicals like 137Cs and 90Sr. [5].
Magnetic nanoparticles bind with contaminants , such as oil and arsenic and removed using a magnet.

## Slide 9
3. Nanocatalysts & redox active nanoparticles:
Nanoparticles serve as catalysts.
Chemically degrade pollutants.
Scientists from IISc, Bangalore-India are evaluating immobilized nano titanium-dioxide particles for degrading organic as well inorganic pollutants.[6]
Nanoscale zerovalent Fe0 & bimetallic Fe0 detoxify organic & inorganic pollutants in aqueous solutions.
Fe0, Fe0/Pt0, Fe0/Pd0, Fe0/Ag0, Fe0/Ni0, Fe0/Co0 can reduce chlorinated alkanes, alkenes, chlorinated benzenes, pesticides, organic dyes, nitro aromatics, nitrates to less toxic and recalcitrant byproducts.[7]

## Slide 10
4.Bioactive nanoparticles:
Being evaluated to decrease use of chemical reagents used for disinfection.
MgO nanoparticles effective against Gram-positive and Gram-negative bacteria.[8]
Silver nanoparticles found effective against both Gram positive and negative. Especially, Staphylococcus aureus, E.coli, Klebsiella pneumoniae and Pseudomonas aeruginosa.

## Slide 11: Two products in India utilizing Bioactive nanoparticles
TATA Swach
Eureka –Forbes AquaSure.

## Slide 12: PRODUCTS IN MARKET
Product | How it works | Importance | Developers
Nanorust to remove arscenic | Magnetic nanoparticles of iron oxide suspended in water bind arscenic, which is then removed with a magnet | India, Bangladesh and other developing countries suffer thousands of cases of arscenic poisoning each year, linked to poisoning of wells. | Rice University, United States.
Desalination membrane | A combination of polymers and nanoparticles that draws in water ions and repels dissolved salts. | Already in the market, this membrane enables desalination with lower energy costs than reverse osmosis. | University of California, Los Angeles and NanoH2O
[9]

## Slide 13
Product | How it works | Importance | Developers
Nanofiltration Membrane | Membrane made up of polymers with a pore size ranging from 0.1-10nm | Field tested to treat drinking water in China and desalinate water in Iran. Using this membrane requires less enrgy than reverse osmosis. | Sachen Industries, Korea.
Nanomesh waterstick | A straw like filtration device that uses carbon nanotubes plaed on a flexible, porous material. | The waterstick cleans the water as it is drunk. Doctors in Africa are using a prototype and the final product is said to be available at an affordable cost in developing countries. | Seldon Laboratories , United States.

## Slide 14
Product | How it works | Importance | Developers
World Filter | Filter using a nanofibre layer, made up of polymers, resins, ceramics and other materials that remove contaminants. | Designed specifically for the household or community level use in developing countries. The filters are effective, easy to use and require no maintenance. | KX Industries, US
Pesticide Filter | Filter using nanosilver to adsorb and then degrade three pesticides commonly found in the Indian water supplies. | Pesticides are often found in the developing countries water supply. This pesticide filter can provide a typical Indian household with 6000 liters of clean water in one year. | Indian Institute of Technology, Chennai, India and Eureka Forbes Limited, India.

## Slide 15: Risks , challenges and opportunities
Potential health and environmental risks.
Integration of nanomaterials into existing water purification systems.
Availability and cost.

## Slide 16: CONCLUSION
Already showing promising results.
Once certain impending hurdles are overcome, will define the modern water purification systems.
Proper studies are to be carried out to assess any harmful effects on environment and living beings.

## Slide 17
References:
1. John Loncto, Marlan Walker and Lynn Foster(2007). Nanotechnology in Water Industry.Nanotechnology Law and Business, June 2007, pp: 157-159.
Peter S. Cartwright. Nanofiltration, When it works for the whole house. URL: http://www.wcponline.com /pdf/Nano.pdf.
O.V. Makarova, C-M. Tang, P. Amstutz, R. Divan, A. Imre, D.C. Mancini, M. Hoffbauer, and T. Williamson, J. Vac. Sci. Technol. B, 27, 2585-2587 (2009). URL: http://nano.anl.gov/news/highlights/2009_nanofilters.html.
Long Beach 90H2O(2010).URL: http://www.lbwater.org/pdf/desal_lbmethod.pdf
www.safewater.org/PDFS/.../Ultrafiltration_Nano_ReverseOsm.pdf .
Katherine Watlington for U.S. Environmental Protection Agency. Emerging Nanotechnologies for Site Remediation and Wastewater Treatment. August 2005, pg 35.

## Slide 18
References…..
Ashok Raichur . Nanoscale water treatment needs innovative engineering. 6 May 2009. URL: http://www.scidev.net/en/new-technologies/nanotechnology-for-clean-water/opinions/nanoscale-water-treatment-needs-innovative-enginee.html
Zhang W.X. 2003, Nanoscale iron particles for environmental remediation. J .Nanoport. Res.5, pp323-332.
Stoimenov P.K., R.L. Klinger, G.L. Marchin & K.J. Klabunde, 2002. Metal oxide nanoparticles as bactericidal agents. Langmuir 2002, 18, pp 6679-6686.
David Grenshaw(2009).Nanotechnology for clean water treatment: Facts and figures. 6-May-2009. URL:www.SciDirect.net.