## Slide 1: SAFETY AIRBAGS IN CARS

## Slide 2: CONTENTS
1 INTRODUCTION
2 BASIS OF AIR BAGS
3 DEVELOPMENTS OF AIR BAGS
4 CONSTRUCTION OF AIR BAGS
5 WORKING
6 MODERN TYPES
7 FUTURE
8 AIR BAG DEPLOYMENT
9 AIR BAG CHECKS
10 DISARMING AIR BAGS
11 CONCLUSION

## Slide 3: INTRODUCTION
Until recently seat belts provided the sole form of passive restraint in cars.
Slowly talks arose about their safety.
Airbags have been under development for many years.
Statistics reveal that airbags reduce the risk of casualty in a DFC by 30%.
Airbags are the subject of serious governments industry research and tests.

## Slide 4
Newton’s second law of motion.
If objects aren’t restrained they will continue moving at the speed of the moving car even if the car is stopped by a collision.
All airbags need to do is to slow down passengers speed.

## Slide 5: DEVELOPMENT
WORLD WAR-2 :saw the first patent on an inflatable crash landing device for airplanes.
1980:first commercial airbags appeared in automobiles.
Ever since 1988 it became a binding.
Efforts to adapt the airbag was stranded due to prohibitive prices and technical hurdles.

## Slide 6: MAIN PARTS OF AN AIRBAG
Bag
Sensor
Inflation system

## Slide 7: BAGS
Is made up of a thin nylon fabric, which is folded into the steering wheel or dashboard or the seat or door.
The powdery substance released ( regular cornstarch or talcum powder) is used to keep the bags lubricated while they’re in storage.

## Slide 8: SENSOR
A device that tells the bag to inflate.
It works with the control module to discriminate between crash and non- crash events.

## Slide 9: INFLATION SYSTEM
NaN3+KNO3=large amts. of NITROGEN GAS.
Hot Blasts of the nitrogen inflate the air bag from its storage site up to 322Kmph.

## Slide 10: CONSTRUCTION OF AIR BAGS
Airbag are assemblies consisting of the airbag (made of Nylon), inflator modules and sensor housing, electrical connectors (Clock spring), airbag retainer and the cover.

## Slide 11: Inflator assembly
Control module activates airbag assembly- electric current is sent to the detonator-ignition of sodium azide pallets-evolves nitrogen gas.

## Slide 12: working
air bags are designed to inflate in frontal impacts in which the car strikes about 16 km/hr
After collision senors sents an electric current to ignitor system
Electric current heats the filament which ignates the capsule which in turn ignites the gas generating pallets
The gas expands quickly and inflation of air bags there by takesplace,which break through a plastic cover in the steering wheel
Time taken for all these things about .1sec.

## Slide 13: DRIVERS SIDE AIRBAG

## Slide 15: Modern types airbags
Curtain airbags
Developed by mercedes and volvo
Inflate infront of windows to provide passengers better head and neck protection
More efficient at tipping and side impacts
Reduce HIC by 80%

## Slide 16
Head throax bag
Developed by ford and renault
High protection to head
ITS
Developed by BMW.
Worlds first airbag for head protection

## Slide 17: Future of airbags
Smart systems
Includes weight sensors
Determine type occupant in seat.ie.child or adult.
Infrared occupant
Detect the distance of passenger from airbags

## Slide 18
Capacitive reflective occupant sensing
Identify distance passenger from dash board
Discriminate between human occupant and inanimate objects
Update sensor
Deploys seatbelt pretensioners faster to get benefit of airbags

## Slide 19
Centralised electronic control unit
New sensor technology through software

## Slide 20: Air bag deployment
Airbag inflation
Depicits contact with airbag
Coming to rest in seat and deflation of airbag
All these take in 30 milliseconds

## Slide 21: Airbags checks
When we turn key look at the dash to find airbag light for 7-10 sec.&then go out
Problems occur when
1. light does not come on
2. if light does not go off after period
3. if light comes during driving

## Slide 22: Disarming airbags
Disconnect battery
Wait 30sec.
Remove airbag fuse
Drop sound insulator panel
Disconnect the circuits
Thus the bag is disarmed
Keep the bag below 130degree celsius

## Slide 25: CONCLUSIONS
Air bags are of greater importance in todays vehicles siince safety of human life is of prior importance
So far safe riding and for saving the precious life the safety bags must be implemented
Let’s hope every automobile manufacturer implements the same